## Slide 1
PROJECT REVIEW 1 | UV GUARD
Smart UV Risk Classification and Ambient Light Monitoring System Using ESP8266 with ThingSpeak Cloud Connectivity
STUDENT NAME
Pravin A
REGISTER NUMBER
722824106121
YEAR / DEPT / SECTION
III Year / ECE / C
COURSE CODE & NAME
U23EC492 - IoT and Application
SDG ADDRESSED
SDG 3 - Good Health & Well-being
SDG 7 - Affordable & Clean Energy
TRL
TRL 4 - Experimental Proof of Concept
REVIEW & DATE
Review 1 |
Supervisor: Dr. S. Ramalingam, AP/ECE | Sri Eshwar College of Engineering, Coimbatore

## Slide 2: Introduction
Invisible risk: UV radiation (100-400 nm) from the Sun cannot be seen or felt, so exposure is easily underestimated.
Health impact: sunburn, photokeratitis, premature skin ageing, cataracts and skin cancer.
Who is exposed: outdoor workers, students and sports participants in tropical India.
Opportunity: an inexpensive analog UV sensor plus the Wi-Fi ESP8266 can warn users where they actually stand.
WHO GLOBAL SOLAR UV INDEX
0-2
Low
3-5
Moderate
6-7
High
8-10
Very High
Objective: a low-cost, portable device that measures UV, classifies risk and alerts the user locally, with optional cloud monitoring.

## Slide 3: Problem Statement
1
UV is invisible and heat does not track its intensity, so risk cannot be judged by eye
2
Weather-app forecasts are regional, not specific to the user's exact spot
3
Professional UV meters are costly and show a bare number to interpret
4
Hobby builds print raw sensor values with no risk level, advice or light context
5
Noisy readings and screen flicker make low-cost displays hard to trust
CORE PROBLEM
Design a low-cost, portable embedded system that continuously measures UV radiation, classifies it into easily understood risk categories, and notifies the user through a display and LEDs, while staying extensible to cloud monitoring.

## Slide 4: Literature Survey
1
Professional UV meters
Calibrated, erythemal-weighted readings; accurate but costly [1]
2
Forecast apps
UV Index estimated from sun angle, ozone and cloud; free but regional [1]
3
Wearable sensors
Personal exposure tracking with phone link; accuracy depends on placement
4
Microcontroller monitors
Arduino/ESP boards with UV sensors; cheap but often uncalibrated raw values
5
IoT weather stations
Multi-sensor nodes with cloud dashboards; no direct local alert
UV SENSOR
Analog (GUVA-S12SD, ML8511) chosen over I2C digital (VEML6075, LTR390, SI1145) for simplicity
CONTROLLER
ESP8266: built-in Wi-Fi at low cost, vs Arduino Uno (no Wi-Fi) and ESP32 (costlier)
NOTIFICATION
Colour TFT plus LEDs preferred over buzzer, OLED or app-only alerts

## Slide 5: Existing Solutions & Gaps Analyzed
Gap in existing solutions | Effect on the user | UV Guard response
High cost of calibrated meters | Out of reach for schools and small farms | Low-cost parts; Rs. 1,400 total build
Regional forecast only | Local exposure unknown | Measures UV at the device location
Raw numbers, no meaning | Risk is hard to understand | 4 named levels with colour and advice
No immediate local alert | Warning may be missed | Green / red LEDs switch instantly
Noisy readings and flicker | Display looks unreliable | Averaging, hysteresis, partial redraw
Unclear calibration | Misleading UV Index claims | Shown as raw ADC; calibration planned
Network dependence | No data when offline | Local alerts work offline; cloud optional

## Slide 6: Proposed Solution: UV Guard
INPUT
PROCESSING
OUTPUT
UV Sensor
analog output to A0
LDR + 10 k
bright / dark to D1
ESP8266 NodeMCU
Sample every 25 ms
1 s average + smoothing
4-level classification
Hysteresis and sensor checks
1.8" TFT dashboard (SPI)
Green / Red LEDs
Wi-Fi to ThingSpeak cloud
LOW
ADC < 100 | Green LED
MODERATE
ADC 100+ | Green LED
HIGH
ADC 200+ | Red LED
VERY HIGH
ADC 300+ | Red LED
Thresholds are placeholders pending calibration; an 8-count hysteresis prevents level flicker.

## Slide 7: Proposed Work Plan
REVIEW 1
Foundation & Hardware
Problem identification and objectives
Literature survey and gap analysis
Component selection: sensor, controller, display
Breadboard assembly; TFT, LDR and UV sensor tests
REVIEW 2
Firmware & Cloud
Sampling, filtering and hysteresis classification
LED alerts and 3-screen TFT dashboard
Wi-Fi and ThingSpeak upload every 16 s
Serial test mode and integration testing
REVIEW 3
Calibration & Demo
Field testing in 5 light conditions
Calibrate against a reference UV meter
Secure upload via HTTPS / MQTT
Enclosure, final report and demo

## Slide 8: References
[1] WHO, WMO, UNEP and ICNIRP, Global Solar UV Index: A Practical Guide. Geneva: WHO, 2002.
[2] Espressif Systems, ESP8266EX Datasheet.
[3] ESP8266 Community, "Arduino core for ESP8266 WiFi chip," GitHub. github.com/esp8266/Arduino
[4] Adafruit Industries, "Adafruit GFX Graphics Library," GitHub.
[5] Adafruit Industries, "Adafruit ST7735 and ST7789 Library," GitHub.
[6] The MathWorks, "ThingSpeak IoT Analytics Platform." thingspeak.com
[7] GenUV, GUVA-S12SD UV Light Sensor Datasheet.
[8] LAPIS Semiconductor, ML8511 UV Sensor with Voltage Output Datasheet.
[9] Vishay Semiconductors, VEML6075 UVA and UVB Light Sensor Datasheet.
[10] Lite-On Technology, LTR-390UV-01 Ambient and UV Light Sensor Datasheet.
[11] Silicon Laboratories, Si1145/46/47 Proximity, UV and Ambient Light Sensor IC Datasheet.
[12] Sitronix Technology, ST7735R 262K Color Single-Chip TFT Controller/Driver Datasheet.

## Slide 9: Work Progress to Date
COMPLETED
✓
Hardware assembly and unit tests
✓
Firmware: sampling, filter, hysteresis
PENDING
Calibrate thresholds with a reference UV meter
Chart: Field test: raw ADC by condition
| Covered | Indoor | Window | Shade | Sunlight
Raw ADC | 2 | 3 | 40 | 120 | 400
Rs. 1,400
total estimated build cost
TRL 4
proof of concept
TFT dashboard (3 screens), no flicker
LED alerts and serial test mode
ThingSpeak upload every 16 s, offline-safe
Field tests in 5 light conditions

## Slide 10
Thank You
Questions and suggestions are welcome
UV Guard | Pravin A | 722824106121