## Slide 1
PROJECT REVIEW 2
Smart UV Risk Classification and Ambient Light Monitoring System Using ESP8266 with ThingSpeak Cloud Connectivity
STUDENT NAME
Pravin A
REGISTER NUMBER
722824106121
YEAR / DEPT / SECTION
III Year / ECE / C
COURSE CODE & NAME
U23EC492 - IoT and Application
SDG ADDRESSED
SDG 3 - Good Health & Well-being
SDG 7 - Affordable & Clean Energy
TECHNOLOGY READINESS LEVEL
TRL 4 - Experimental Proof of Concept
REVIEW & DATE
Review 2 |
Supervisor: Dr. S. Ramalingam, AP/ECE | Sri Eshwar College of Engineering, Coimbatore

## Slide 2: Introduction
BACKGROUND
UV radiation (100-400 nm) is invisible; UVA and UVB reach the ground
Causes sunburn, photokeratitis, skin ageing, cataracts, skin cancer
MOTIVATION & IMPORTANCE
Strong year-round UV in tropical India; outdoor workers and students exposed
Forecasts are regional; calibrated meters are costly
TECHNICAL CONTEXT
ESP8266 NodeMCU reads an analog UV sensor (10-bit ADC, 0-1023)
LDR light state, TFT + LEDs, ThingSpeak upload over Wi-Fi
PROJECT OBJECTIVES
Measure, filter and classify UV into 4 levels with hysteresis
Local TFT/LED alert; 16 s cloud upload; works offline; test mode

## Slide 3: Problem Statement
THE PROBLEM
UV cannot be seen or felt, so safe/unsafe levels cannot be judged by eye
No affordable, local, real-time notification between forecasts and costly meters
Hobby designs print raw values: no risk level, advice or light context
IMPACT
Exposure is underestimated, even on hazy or cloudy days
Risk of sunburn, eye damage and skin cancer for outdoor workers and students
Uncalibrated 'UV Index' claims can mislead users
NEED FOR THE SOLUTION
Low-cost, portable, local UV measurement
Named risk levels with colour, LEDs and advice
Stable readings; no display flicker
Works offline; cloud monitoring optional

## Slide 4: Literature Survey
Approach | Methodology | Findings / strengths | Limitations
Professional UV meters | Calibrated detector with erythemal weighting | Most trustworthy local readings | High cost; needs trained interpretation
Forecast apps / websites | UV Index estimated from solar elevation, ozone, cloud | Free and widely available | Regional; ignores shade, reflection, altitude
Wearable UV sensors | Body-worn sensors or patches with phone link | Personal exposure tracking | Orientation-dependent accuracy; consumer products
Microcontroller UV monitors | Analog/digital UV sensor on Arduino/ESP; serial, LCD/OLED; ThingSpeak or Blynk | Low cost and flexible | Raw voltages shown as UV Index; calibration not described
IoT environmental stations | Multi-sensor node (UV, temperature, humidity, pressure) to cloud | Long-term records | Needs network to view; no local alert

## Slide 5: Existing Solutions & Gaps Analyzed
EXISTING APPROACHES AND LIMITS
Professional meters: accurate but costly, number only
Forecast apps: regional, not at the user's spot
Wearables: placement-dependent, single-purpose
Hobby monitors: raw values, uncalibrated, basic UI
IoT stations: network-dependent, no local alert
Unfiltered ADC noise; full-screen redraw flicker
GAPS ADDRESSED BY UV GUARD
Local, low-cost UV sensing at the device
Four named levels with colour and advice
Instant green/red LED alert
Averaging, smoothing, hysteresis, partial redraw
LDR bright/dark context for readings
Local operation continues without Wi-Fi
Value labelled as raw ADC until calibrated

## Slide 6: Proposed Solution
Sample UV on A0 every 25 ms
Classify L1-L4 with hysteresis
Update TFT and LEDs
Upload to ThingSpeak every 16 s
IMPLEMENTED (per report)
4 levels: LOW, MODERATE, HIGH, VERY HIGH (placeholder thresholds 100/200/300)
LDR bright/dark with 3 s debounce
PLANNED (not yet done)
Calibration against a reference UV meter, then real UV Index
3-screen TFT dashboard; green (L1-2) / red (L3-4) LEDs
NO SIGNAL / SATURATED sensor checks
Serial test mode (levels forced 15 s)
ThingSpeak upload; offline operation
Battery operation and mobile app
Richer dashboard: history, daily maximum

## Slide 7: Proposed Work Plan
REVIEW 1
Planned and completed
COMPLETED
Problem definition, objectives
Literature survey, gap analysis
Component and sensor selection
Breadboard assembly; TFT, LDR, UV sensor tests
REVIEW 2
Current implementation
IN PROGRESS
LED alerts, TFT screens, test mode
ThingSpeak upload; field tests (preliminary)
Prototype housing shown in photos
REVIEW 3
Remaining tasks
PLANNED
Calibrate against reference UV meter
Integration and re-testing
Final report, demo, deliverables

## Slide 8: Block Diagram

## Slide 9: Prototype Image (Hardware)
dotboard prototype: NodeMCU, TFT, UV sensor, LDR, LEDs
VISIBLE IN PHOTOS
NodeMCU ESP8266
1.8" ST7735 TFT
UV sensor and LDR
Green and red LEDs
3D-printed case with QR label
USB power cable
Report lists an enclosure as future work, but the cost sheet includes a 3D-printed case. Confirm.

## Slide 10: Prototype Image (Software)
Arduino IDE serial monitor: raw, level, light, sensor, cloud status; cloud upload entries
No simulation outputs are in the report. Circuit diagram (Fig. 6) and block diagram (Fig. 4) appear in the report.

## Slide 11: Technology Stack Used
CONTROLLER & SENSORS
NodeMCU ESP8266 (ESP-12E), 80 MHz, Wi-Fi
Analog UV sensor (GUVA-S12SD or similar)
5 mm LDR with 10 k divider
DISPLAY & ALERTS
1.8" 128x160 ST7735 SPI TFT
Green and red LEDs (220 ohm)
3D-printed enclosure (cost sheet)
COMMUNICATION
ADC (A0), GPIO, hardware SPI
UART / USB serial, 115200 baud
Wi-Fi 802.11 b/g/n; HTTP over TCP/IP
SOFTWARE
C++ on Arduino framework; Arduino IDE
ESP8266 core, ESP8266WiFi, HTTPClient
Adafruit GFX, ST7735/ST7789, SPI
CLOUD
ThingSpeak channel (3 fields)
Upload every 16 s (free tier limit)
Credentials kept in secrets.h
SIMULATION TOOLS
None stated in the report
Testing by serial monitor and field readings

## Slide 12: Uniqueness Claimed
Feature | Forecast apps | Typical microcontroller UV monitors | UV Guard (this project)
Where UV is sensed | Regional estimate | At the device | At the device
Result shown | UV Index forecast | Often raw sensor value | 4 named levels, colour, advice
Immediate local alert | App must be opened | Serial / LCD output | Green / red LEDs and TFT
Noise handling | Not applicable | Often unfiltered | Averaging, smoothing, hysteresis
Ambient-light context | No | Rarely | LDR bright/dark (debounced)
Works offline | Needs internet | Depends on design | Yes; cloud optional
Calibration honesty | Not applicable | Raw often shown as UV Index | Labelled raw ADC; not a certified meter
Claim: practical integration of filtering, hysteresis, dual local alerts, offline operation and honest labelling at about Rs. 1,400-1,450. Not claimed as a new sensing method.

## Slide 13: Specifications: Hardware Components
S.No. | Hardware Components | Specifications | Cost (Rs.)
1 | NodeMCU ESP8266 (ESP-12E) x1 | 80 MHz, integrated Wi-Fi, USB, 10-bit ADC (A0) | 350
2 | Analog UV sensor x1 | Analog output to A0; exact model to be confirmed | 200
3 | 1.8" TFT, ST7735 x1 | 128 x 160, SPI, 3.3 V, landscape use | 370
4 | 5 mm LDR x1 | Two-terminal; bright/dark input on D1 | 40
5 | Resistors: 10 k x1, 220 ohm x2 | LDR divider; LED current limiting | 10
6 | Green LED x1, Red LED x1 | On D2 (levels 1-2) and D0 (levels 3-4) | 10
7 | Jumper wires | As required | 100
8 | Dotboard | 1 piece, circuit assembly | 100
9 | USB cable | Programming and 5 V power | 100
10 | 3D-printed case x1 | Enclosure (cost sheet only) | 150
11 | Product sticker x1 | Label | 20
 | Total (sum of line items) |  | 1,400

## Slide 14: References
[1] WHO, WMO, UNEP and ICNIRP, Global Solar UV Index: A Practical Guide. Geneva: WHO, 2002.
[2] Espressif Systems, ESP8266EX Datasheet.
[3] ESP8266 Community, "Arduino core for ESP8266 WiFi chip," GitHub. https://github.com/esp8266/Arduino
[4] Adafruit Industries, "Adafruit GFX Graphics Library," GitHub. https://github.com/adafruit/Adafruit-GFX-Library
[5] Adafruit Industries, "Adafruit ST7735 and ST7789 Library," GitHub. https://github.com/adafruit/Adafruit-ST7735-Library
[6] The MathWorks, "ThingSpeak IoT Analytics Platform." https://thingspeak.com
[7] GenUV, GUVA-S12SD UV Light Sensor Datasheet.
[8] LAPIS Semiconductor, ML8511 UV Sensor with Voltage Output Datasheet.
[9] Vishay Semiconductors, VEML6075 UVA and UVB Light Sensor with I2C Interface Datasheet.
[10] Lite-On Technology, LTR-390UV-01 Ambient and UV Light Sensor Datasheet.
[11] Silicon Laboratories, Si1145/46/47 Proximity, UV and Ambient Light Sensor IC Datasheet.
[12] Sitronix Technology, ST7735R 262K Color Single-Chip TFT Controller/Driver Datasheet.

## Slide 15: Work Progress to Date
COMPLETED
✓
Hardware assembly and unit tests
✓
Firmware: sampling, filter, hysteresis
✓
TFT dashboard (3 screens), LEDs, test mode
✓
ThingSpeak upload; offline operation
✓
Field tests in 5 conditions (preliminary)
ONGOING
Calibration vs reference UV meter (not yet done)
Chart: Preliminary field test: raw ADC
| Covered | Indoor | Window | Shade | Sunlight
Raw ADC | 2 | 3 | 40 | 120 | 400
Values are raw ADC counts; thresholds are placeholders, so levels are 'sensor risk', not UV Index. Report lists the shade reading (120) with light state 'off' - confirm.
3D print enclosure

## Slide 16
Thank You
Questions and suggestions are welcome
UV Guard | Pravin A | 722824106121